## Slide 1: Operator Training ReAccelerator Controls (Part 2 of 2)
Tasha Summers Accelerator Controls Physicist III

## Slide 2: Outline
Topics for Today
  ReAccelerator Launch and Status pages
  Device controls: Magnets, RF, diagnostics
  Performing an energy change
  Monitoring and troubleshooting during an experiment

## Slide 3: ReA Interfaces: Launch Screen
Getting to the ReA Launch page:
Best to work in OPI Runtime
Perspective
Select REA
from top-level
menu
Organized by
system (top)
area (bottom)
expert (2nd tab)
All buttons here open
other pages

## Slide 4: ReA Interfaces: Expected Use
For monitoring always have open:
  Status Page
  Beast
For tuning
  Operator page updated for specific experiment
  Top-level area overviews

## Slide 5: ReAccelerator Status
  Top section – beam and experiment information and history
  Middle section – equipment status with focus on on/off, in/out
    need to add D-Line
    areas not in use changed to grey
    switch to official device shapes
  Middle section – equipment summaries, important values
Expect Status page to be updated frequently for next couple months.
Some colors will be adjusted to make problems more obvious.
Summary sections at bottom will be expanded/rearranged.

## Slide 6: Device Controls: Magnets
2 main ways of accessing magnet/power supply controls
  Overview/ and OpsTuners (High-level and power supply)
  Use high-level pages – provide ‘tuning’ alarms and physics info
    also combine multiple power supplies for electrostats

## Slide 7: Control Pages: Magnets
Pop-out the section into another tab or window
‘More…’ button has links to Device (magnet/electrostat) details and to power supply details
Readback column will have alarm-sensitive border for set/read mismatch

## Slide 8: Control Pages: Magnet Details
Electrostat details
Power Supply details
Magnet details
Access operator and alarm limits

## Slide 9: Control Pages: RF and Details
Currently 2 main ways of accessing RF status and controls
  Overview and OpsTuners

## Slide 10: Control Pages: Diagnostics
Available on Area Overview pages or Diagnostics Overview

## Slide 11: Operator Overview Pages
Status and common controls for a section of the accelerator
  These are next on the list of pages to update so they may change significantly in the next few months.

## Slide 12: Energy Change: at a glance
Establish State
Scale L-Line
Change Energy & Verify Matching
Re-establish State & Record Process

## Slide 13: Energy Change: Establish State
Establish State
  Check and clear alarms
  Verify that beam scaling channels are where they should be

## Slide 14: Energy Change: Establish state cont.
Checking notable information
  Status Page
  Beast
  Operator Page
  Experiment count rate..
  Slit gaps, position..
  RF stability…
  Dipole Drift…
  Non-tuning alarms…

## Slide 15: Energy Change: Establish state cont.
Establish State
  Check and clear alarms
  Verify that beam scaling channels are where they should be
  Check notable information
  Make a Saveset
    Make sure devices that are OFF have setting of zero
    Scroll through the saveset, make sure no errors pop out at you
    Make sure to refresh, and that you can find the save after having done so
  Change hourlog state to PDT once you have the beam
Saveset picture

## Slide 16: Energy Change: Scaling
Scale L-Line
  Reference provided charts
    Verify target parameters are correct with experimenters, logbook, or special instructions
    ‘projects/rea3/rea3-experiments/<exp# PI>’
      Should have beam parameters, mass, charge, brho, energy steps, extra comments
      Secondary sheets may have tabled, pre-calculated, dipole field values with reference to intended energy steps

## Slide 17: Energy Change: Scaling cont.
Scale L-Line
  Verify target parameters are correct with experimenters, logbook, or special instructions
  Set target values
    Set Scaling channel(s) (Beam Energy)
      Tuning alarms should alarm, as are now off from intended values
    Set the quads/steerers to their intended values (based on scaling channel values) by hitting ‘set’
        tuning alarms should go away once they’ve reach their intended values

## Slide 18: Energy Change: Scaling cont.
Scale L-Line
  Verify target parameters are correct with experimenters, logbook, or special instructions
  Set target values
    Set Scaling channel(s) (Beam Energy)
      Tuning alarms should alarm, as are now off from intended values
    Set the quads/steerers to their intended values (based on scaling channel values) by hitting ‘set’
        tuning alarms should go away once they’ve reach their intended values
    Dipole Matching
      ‘match’ dipoles, make sure that they’re reaching their pre-calculated values
        if not, cycle as needed and walk them to correct value
  Update hourlog with new beam energy

## Slide 19: Energy Change: Cavity Amplitude & Matching
Cavity Amplitude & Matching
  Decide on verification
    S-Bend Slits (D1166), with intermediate quads turned off
    D1316 slits, either on transmission or by image
    Experimenter’s detector

## Slide 20: Energy Change: Cavity Amplitude & Matching cont.
Cavity Amplitude & Matching
  Decide on verification
  Change amplitude of last cavity
    optimize using given method of verification

## Slide 21: Energy Change: Cavity Amplitude & Matching cont.
Cavity Amplitude & Matching
  Change amplitude of last cavity
  Make sure your matched from LINAC exit into L-Line
    Turn off D1155 dipole
    Tune (LINAC solenoids and correctors) to get %50-%70 transmission through L110-R and AP_D1163 5mm apertures and onto FC_D1164 in ‘The Stub’
    Turn back on the D1155 dipole, making sure it’s field value returns

## Slide 22: Energy Change: Cavity Amplitude & Matching cont.
Cavity Amplitude & Matching
  Decide on verification
    S-Bend Slits, with intermediate quads turned off
    D1316 slits, either on transmission or by image
    Experimenter’s detector
  Change amplitude of last cavity
    optimize using given method of verification
  Make sure your matched from LINAC exit into L-Line
    Turn off D1155 dipole
    Tune (LINAC solenoids and correctors) to get %50-%70 transmission through L110-R and AP_D1163 5mm apertures and onto FC_D1164 in ‘The Stub’
    Turn back on the D1155 dipole, making sure it’s field value returns
  Double Check the amplitude setting
    To make sure it wasn’t the cavities effect on trajectory that is being optimized for transmission, may have to repeat last two steps a few times

## Slide 23: Energy Change: Re-establish, record, & deliver
Re-establish State, Record & Deliver
  Does the beam make it through previously set slit positions/gaps
  Does beam make it to the end?
  What are the count rates of merit, have you restored these rates?
  Do you still meet trajectory and position requirements for experiment?
  IFF it’s good, make sure any tuning alarms made in this process are cleared (or accepted), that anything turned off is also set to zero, and that a saveset is made.
  Speak with experimenters, are they happy with it?
  Update Hourlog to EXR when beam is returned to experiment.

## Slide 24: ReA Operator Page
Updated for every experiment to provide the most used controls

## Slide 25: Troubleshooting – EBIT and Q/A
Look at addition to the obvious:
  Status page for obvious: equipment on? valves open?
  Use save/restore program to see if something changed
  Check Beast for alarms (see alarm guidance if available)
EBIT-specific
  Check if there is electron source current
Transport lines
  Check on FCs to see where beam is lost
[Get info Alain sent]

## Slide 26: Troubleshooting – RFQ/Linac
RFQ
  Is it tripping? Amplitude will drop out and automatically reset
  Look for pulsing on scope (Windows computer in corner)
  [picture of scope trace?]
Linac
  Did something trip? Maybe there’s a set/read error?
  Look on FCs at start and end of linac for where beam is lost
  Turn off the dipole at the end of the platform (D1155) and check for beam on FC_D1164

## Slide 27: Troubleshooting – HEBT
Things blocking beam
  Aperture in or slits closed?
  User beam stop closed?

## Slide 28: Thanks!
Special thanks to Dan Crisp and Mathias Steiner for working on the controls and to Sam Nash, Alain Lapierre and Antonio Villari for testing everything.
Notes: There may be Timbits.